## Slide 1: Identifying Whether an Immediate Value is Valid
Asst. Prof. Mohamed M. Sabry Aly

## Slide 2: The Challenge in Immediate values
Instruction length: 32 bits
  For opcode and operands  12 bits for immediate field
  Register is 32 bits wide, how can we fill 12 bits in 32 bits?
0
31
OpCode
Operands (registers)
Immediate
28
24
21
19
16
15
12
11
8
7
Instruction format in ARM processor (further details in Chapter 8)

## Slide 3: How to determine if Immediate value is Valid?
Examples
  MOV R0,#0x258
  MOV R0,#0x254
  MOV R0,#0x152
Step 1: Get all numbers in Binary
  0010 0101 1000
  0010 0101 0100
  0001 0101 0010

## Slide 4: How to determine if Immediate value is Valid?
Step 2: Identify the indices of least significant and most significant ones (m,n)
Idx 87 654 3210
  0010 0101 1000 m=8, n=3
  0010 0101 0100 m=8, n=2
  0001 0101 0010 m=7, n=1
Step 3: Get the number of bits from least to most significant 1: X=m-n+1

## Slide 5: How to determine if Immediate value is Valid?
Step 3: Get the number of bits from least to most significant 1: X=m-n+1
  X= 9 – 3 + 1 = 7
  X= 9 – 2 + 1 = 8
  X= 8 – 1 + 1 = 8
Step 4: Apply the following Rule:
  If X < 8: valid, else if X > 8: not valid, else: go to step 5
  X = 7 <8  valid
  X = 8  Step 5
  X = 8  Step 5

## Slide 6: How to determine if Immediate value is Valid?
Step 5: Count the number of 0s on the right hand side of the least significant 1 (k)
Idx 87 654 3210
  0010 0101 1000 No need, valid immediate (step 4)
  0010 0101 0100 k = 2
  0001 0101 0010 k = 1
Step 7: if k is even: valid, else: invalid
  No need, valid immediate (step 4)
  k = 2, even  valid
  k = 1, odd  invalid

## Slide 7: Note
This approach is applicable when m < 25
For negative numbers with majority 0XFFF…, the approach is applied on the complement of such number