## Slide 1: Introduction on Digital\Analog (DA) Trainer Set
1kohm and 100kohm potentiometer
The Power Supply
The Function Generator
General introduction on the DA trainer set
16 bit Data Swtich
Pulse switch
Adapter
16 bit LED Display
Power “on/off” Switch
The Breadboard
The Digital Display

## Slide 2: Introduction on the Power Supply
C
The Power Supply provides a
(i) Fixed : +5V and -5V
Four turn-pins are internally connected
(ii) Variable Voltages : 0 to +15V
and 0 to -15V.
(iii) Ground point
Four turn-pins are internally connected
C
Turn knob C to vary the voltage from 0 to ±15V.

## Slide 3: Introduction on the Function Generator
The Function Generator provides
(i) Fixed TTL : +2.8V to +5V
Four turn-pins are internally connected
Four turn-pins are internally connected
(ii) Ground point and
(iii) Output waveform
D
E
F
G
The Output waveform is determined by adjusting the Function knob D and the amplitude can be increase and decrease by adjusting the Amplitude knob G.
D
G
The TTL and Output frequency can be
adjusted by setting the Freq.Range
knob E and adjusting the Freq. Var.
(fine) knob F.
Frequency Range
X1 : 1Hz ~ 10Hz
X10 : 10Hz ~ 100Hz
X100 : 100Hz ~ 1Khz
X1K : 1Khz ~ 10Khz
X10K : 10Khz ~ 100Khz
E
F

## Slide 4: Introduction on the 16 Bit Data Switch
There are 16 set of Data/Toggle Switches. When the switch is set to 0
position , the output is at LO LEVEL
and the LED will turn off.
LED turn OFF
LED turn ON
2. When the switch is set to 1
position , the output is at HI LEVEL
and the LED will turn on.

## Slide 5: Introduction on the Adapter
The Adapter provides :-
(i) Ground point
BNC cable connected to CH1 of oscilloscope
1-BNC , connected to CH1 of the
oscilloscope.
Signal input from TTL/IC chip
BNC cable connected to CH2 of oscilloscope
Signal input from IC chip
2-BNC , connected to CH2 of the
oscilloscope.

## Slide 6: Introduction on the 16 Bit LED Display
The are 16 Bit LED Display.
When at HI LEVEL the LED will turn on.
It will turn off when at LO LEVEL.
Six turn-pins are internally connected
LED off = LO LEVEL
LED on = HI LEVEL